## Slide 1: The CO2MPAS tool
Ispra, 17/11/2016
G. Fontaras,
V. Arcidiacono, V. Valverde, K. Anagnostopoulos, S. Tsiakmakis, B. Ciuffo, J. Pavlovic, D. Komnos

## Slide 2: Approach – Phasing-in
During the WLTP phasing-in, WLTP measurements will be correlated into NEDC values using CO2MPAS (CO2 Model for PAssenger and commercial vehicles Simulation), developed by JRC.
WLTP-based vehicle Type-Approval
CO2MPAS meta-model
NEDC-equivalent CO2 emissions
NEDC-based OEM performance

## Slide 3: CO2MPAS data flow overview
Data Entry
Reporting
Veh. characteristics
WLTP Bag CO2
WLTP time series
Processing
Sub models calibration
NEDC simulation
Simulated time-series
Summary Report
Dice report

## Slide 4: Key features
Comprises of 2 main calculation modules
Power – RPM module
Simple longitudinal dynamics (WLTP-GTR)
Engine power and RPM calc’d @ 1hz
Inclusion of Mech or Elec. loads where needed
Generic start-stop logic
A/T and CVT RPM prediction model
Alternator logic calibrated over WLTP
FC module
Calculation of FC
  Indicative instantaneous approach
Based on an extended Willans model
Semi-physical empirical cold start model
Calibration - Optimization based on WLTP results
Specific engine technologies included
Accurate calculation of average / instantaneous power demand
Very good accuracy when compared with results obtained from the Cruise simulations by LAT and Real test data from 40 vehicles
+Parallel work for HEV control module and optimization

## Slide 5
Gearshifting / Engine RPM pred. Logic
Currents Alternator
CurrentsBattery
Fuel Consumption Model
FCM
Optimization
Total Engine Power Demand Model
Engine Temperature model
Engine RPM Model
WLTP CO2 (Initial estimate)
WLTP CO2 (Calibrated)
Electric power demand
Power demand @ the wheel
Electrical System Logic
Engine
Torque Losses
Cycle Prediction
Cycle, Road loads & Vehicle Characteristics
WLTP measurements
(Bag CO2 & Timeseries signals)
Losses GB
Losses Differential
Losses TC / Clutch

## Slide 6: CO2MPAS sub-models
CO2MPAS includes the following sub-models:
    Automatic Transmission model (gear shifting)
    Clutch / Torque converter model score
    Engine cold start speed model
    Engine speed model
    Start stop model
    Alternator model
    Engine coolant temperature model
    Engine fuel consumption (CO2 ) model

## Slide 7: CO2MPAS self assessment of internal models
Mean absolute error (quantities with units)
Calibration coefficient for unit-less quantities

## Slide 8: Automatic Transmission model (gear-shifting 1/2)
There are 2 official options enabled in the A/T model:
    Corrected Mean Velocity (CMV) creates a “map” of gear upshifts and down-speeds as a function of vehicle speed.
    GearShift Power-Velocity (GSPV) creates a map of gear upshifts as a function of vehicle speed & the power at the gearbox
CO2MPAS automatically selects the option that better reproduces gear shifting over WLTP
Two sets of gear-shift maps are calculated, hot and cold conditions
In engineering mode the DT option can be also enabled
GSPV example
Power (kw)
Velocity (km/h)

## Slide 9: Automatic Transmission model (gear-shifting 2/2)
Final step: Matrix Velocity Limits (MVL) correction model corrects gear-shifting over quasi-steady state conditions ()
Chart: Engine speed [RPM]
Chart: Engine speed [RPM]

## Slide 10: Automatic Transmission model (gear-shifting 2/2)
For CVTs a gradient boost regressor is used to predict Engine RPM as a function of vehicle speed, acceleration and power at the gearbox
Chart: Time [s]
Chart: Vehicle Speed (km/h)

## Slide 11: Clutch / Torque converter model
CO2MPAS by default calibrates a clutch model (generic or DTC) unless a TC is declared as present on the vehicle:
    In both cases an “RPM-slip” model as a function of acceleration is fitted based on experimental data
Efficiency model (predefined non calibrated):
    Clutch: linear TC efficiency as a function of RPM ratio
    TC: a non-linear efficiency as a function of RPM ratio
For TCs a lock up velocity (48km/h) is used

## Slide 12: Engine cold start speed model
The ECSSM increases idling RPMs during the cold start phase
An optimizer is used to calculate the unit less ΔRPMidle [%] function during cold start
ΔRPM is a linear function o f engine temperature capped at a certain value which is also estimated by the optimizer
Chart: Engine temperature C
 | 118.7457 | 118.7457 | 118.7457 | 118.7457 | 118.7457 | 118.7457 | 118.7457 | 118.7457 | 118.7457 | 118.7457 | 118.7457 | 118.7457 | 118.7457 | 118.7457 | 114.1313 | 25 | 0 | 0
Examples

## Slide 13: Engine speed model
The ESM calculates the exact RPM/Velocity ratios over the specific test
Gear ratios (or default RPM/V ratios) and information on tyre dimensions provided by the user are used as starting values
An optimizer calculates the optimal dynamic radius of the tire based on the dyno velocity and engine RPM data measured over the WLTP

## Slide 14: Start stop model
The SS model defines where the engine should be switched off for SS equipped vehicles
CO2 MPAS uses a classifier in order to associate engine switch off events to vehicle deceleration and velocity.
SS functionality is initiated based on the user provided input on engine SS initiation time
Chart: 

## Slide 15: Alternator model
Comprises of 2 parts:
    Logic part (when the alternator operates and how)
    Electric part (what current is supplied by the alternator)
Logic part identifies different phases (idling, regenerative braking, battery charging, battery depletion) and under what conditions those occur  result: alternator status
Electric part identifies the current per each phase based on other parameters (eg RPM, Battery SOC, deceleration)
A gradient boost regressor is used for predicting the currents based on alt. status, acceleration, power at g/box, SOC at t-1, and initialization time

## Slide 16: Alternator logic and current prediction
Chart: Time

## Slide 17: Alternator logic and current prediction -windows

## Slide 18: Engine coolant temperature model
CO2MPAS uses a regressor to predict engine temperature (T) evolution
Ti is function of Ti-1 , RPM, acceleration and the power at the gearbox
The regressor is calibrated based on WLTP recorded time series using Gradient Boost algorithm (ransac algorithm used for inlier and outlier detection)

## Slide 19: Engine fuel consumption (CO2) model
Extended Willans Model approach:
Fitting of a specific non-linear Willans model
BMEP=(a+b×cm+c×cm2)×FuMEP+(a2×FuMEP2)+l0+l2×cm2
Where:
    BMEP: brake mean effective pressure
    cm: mean piston speed
    FuMEP: fuel mean effective pressure
    a, b, c, a2, l0, l2 are the parameters that are being fitted

## Slide 20: Fuel Consumption (Fc) Calculation Function
, where:
  The following are considered as knowns from the measurement / other COMPAS modules (in order to understand issues and improve the stability of the FC module):
  Engine Speed, Temperature, Engine Power
  The constant parameters are calculated by optimization of the above equation against WLTP CO2 measured data
Engine fuel consumption (CO2) model
Cold start factor

## Slide 21: Engine fuel consumption (CO2) model
Extended Willans Model is calibrated using WLTP CO2 results
    An initial estimate is made based on generic values (categorized per engine and aspiration type)
    The model perturbates until the initial and final estimate of the CO2 time series converge
    A final optimization is done in order to reduce the error in the WLTP bag value prediction.
Specific technologies are currently considered using the Extended Willans approach
    For Petrol engines: Variable valve actuation, Lean combustion, Aspiration type, Cylinder deactivation (limited validation), External EGR (limited validation)
    For Diesel engines: External EGR, Cylinder deactivation (limited validatipn), Selective catalytic reduction (limited validation)

## Slide 22: Optimization path
Rescaling
Initial guess
Optimization

## Slide 23: Summary

## Slide 24: Correlation and CO2MPAS Process flow chart
Yes
Yes
No
WLTP Test Data
TA data – NEDC DV – TA Doc.
Dice report emailed to Timestamp Server
NEDC to be tested?
Physical NEDC Test
No – Accept DV, Add Hash in TA doc
> 0.96
Input CO2MPAS GUI
Generic Values Selection
Sub models calibration (Eng. Temp., RPM, G/box, Clutch-TC, Power)
WLTP CO2 Improving?
Engine - CO2 model calibration / Instantaneous samples
Initial Engine -CO2 model setup
Engine - CO2 model trimming / WLTP bag values
Yes - Engine data. update
No
Final Engine -Vehicle model setup
WLTP (prediction) & NEDC Test simulation
WLTP & NEDC sim. data
Reports (Summary, Dice)
NEDC TA
DF & VF
TA Report

## Slide 25: Correlation and CO2MPAS Process flow chart
Yes
Yes
No
No – Accept DV, Add Hash in TA doc
WLTP Test Data
TA data – NEDC DV – TA Doc.
Dice report emailed to Timestamp Server
NEDC to be tested?
Physical NEDC Test
CO2CO2MPAS <1.04 · CO2DV
NEDC TA
DF & VF
TA Report
Procedures’ Space
Input CO2MPAS GUI
Generic Values Selection
Sub models calibration (Eng. Temp., RPM, G/box, Clutch-TC, Power)
WLTP CO2 Improving?
Engine - CO2 model calibration / Instantaneous samples
Initial Engine -CO2 model setup
Engine - CO2 model trimming / WLTP bag values
Yes - Engine data. update
No
Final Engine -Vehicle model setup
WLTP (prediction) & NEDC Test simulation
WLTP & NEDC sim. data
Reports (Summary, Dice)

## Slide 26: Correlation and CO2MPAS Process flow chart
Yes
Yes
No
WLTP Test Data
TA data – NEDC DV – TA Doc.
Dice report emailed to Timestamp Server
NEDC to be tested?
Physical NEDC Test
No – Accept DV, Add Hash in TA doc
> 0.96
Input CO2MPAS GUI
Generic Values Selection
Sub models calibration (Eng. Temp., RPM, G/box, Clutch-TC, Power)
WLTP CO2 Improving?
Engine - CO2 model calibration / Instantaneous samples
Initial Engine -CO2 model setup
Engine - CO2 model trimming / WLTP bag values
Yes - Engine data. update
No
Final Engine -Vehicle model setup
WLTP (prediction) & NEDC Test simulation
WLTP & NEDC sim. data
Reports (Summary, Dice)
NEDC TA
DF & VF
TA Report

## Slide 27: Stay in touch
JRC Science Hub: www.ec.europa.eu/jrc
Twitter: @EU_ScienceHub
LinkedIn: european-commission-joint-research-centre
YouTube: JRC Audiovisuals
Vimeo: Science@EC
https://co2mpas.io
co2mpas@jrc.ec.europa.eu

## Slide 28: Validation against 39 real cars
Results within +-4%
MT: Manual Transmission, AT: Automatic transmission, CVT: constant variable transmission

## Slide 29: Validation against 39 real cars

## Slide 30: Evaluation AT model options
Method | Top Performance | Average Performance | Prediction vs Calibration | Computational Time
Decision Tree | Good | Good | Bad | Good
CMV | Neutral | Good | Good | Bad
GSPV | Neutral | Neutral | Good | Good
GSPV appears to offer the most advantages
Decision tree gives good results but is unstable
JRC proposal is to use the best of CMV – GSPV, identified on
a case by case basis (see ex – post analysis)

## Slide 31: CO2 Results on selected profiles
Vehicle | Cycle | Validation CO2 | Error (g/km) corrected matrix velocity | Error (g/km) corrected matrix power velocity | Error (g/km) corrected matrix velocity hot/cold | Error (g/km) corrected matrix power velocity hot/cold | Error (g/km) decision tree | Error (g/km) decision tree power | Error (g/km) decision tree temperature | Error (g/km) decision tree temperature power
BMW 328i | NEDC | 170.7 | - | 1.4 | - | 1.2 | - | - | 2 | -
 | WLTP | 193.7 | - | -0.7 | - | - | - | - | -0.2 | -
AUDI A8 | NEDC | 169.7 | 3.1 | - | 2.8 | - | - | - | 1.6 | 1.8
 | WLTP | 189.5 | - | - | 0.9 | - | - | - | 0.2 | -
Mercedes E350 | NEDC | 174.6 | 0.4 | 0.6 | - | - | 1.5 | - | - | -
 | WLTP | 203.1 | - | 0.1 | - | - | -0.4 | - | - | -
Opel Mokka | NEDC | 161.9 | - | - | 0.6 | 0.9 | 3.4 | - | - | -
 | WLTP | 171.7 | - | - | -1.4 | - | 0.1 | - | - | -
Smart ForTwo | NEDC | 105.9 | 2.9 | - | 2.8 | - | - | - | 2.9 | 2
 | WLTP | 131 | - | - | 1.9 | - | - | - | 1.7 | -
Volvo V40 | NEDC | 220.9 | 2.3 | - | - | - | 1.6 | - | 1.7 | -
 | WLTP | 222.2 | -1.6 | - | - | - | -0.5 | - | - | -
Average | NEDC |  | 2.2 | 1.0 | 2.1 | 1.1 | 2.2 |  | 2.1 | 1.9
 | WLTP |  | -1.6 | -0.3 | 0.5 |  | -0.3 |  | 0.6 | 
For vehicle the DT was studied separately from the other two methods
The methods with the best score over NEDC and WLTP were selected
Simulations were run with both (WLTP & NEDC best case)
The error introduced from not selecting the best NEDC case but relying solely on WLTP best case is in the order of 0.2-0.4g/km.
NEDC appears to be overestimated by 1.5g/km. An equal compensation can be applied in the final results.

## Slide 32: JRC proposal
CMV – CMPV appear to be more stable, all present the same error range in NEDC CO2 prediction
Proposal to use CMV-CMPV in the batch runs and final compas version, selection to be made based on the best WLTP performance
Based on the current analysis JRC proposes to adopt the following correction
  NEDCfinal = NEDCcompas predicted – absolute (Errorwltp prediction)
Where: Errorwltp prediction = CO2compas estimation with OBD RPM – CO2 compas estimation with A/T tool RPM
  In all cases COMPAS calibration is done based on OBD recorded RPMs
End results will look like this:
Vehicle | Cycle | Error (g/km) corrected matrix velocity | Error (g/km) corrected matrix power velocity | Error (g/km) corrected matrix velocity hot/cold | Error (g/km) corrected matrix power velocity hot/cold
BMW 328i | NEDC |  | 0.7 |  | 
AUDI A8 | NEDC |  |  | 1.9 | 
Mercedes E350 | NEDC |  | 0.5 |  | 
Opel Mokka | NEDC |  |  | -0.8 | 
Smart ForTwo | NEDC |  |  | 0.9 | 
Volvo V40 | NEDC | 0.7 |  |  | 
Average | NEDC | 0.7 | 0.6 | 0.7 | 

## Slide 33
Chart: Acceleration (m/sec2)
Chart: Time (s)
TC